## Slide 1: CSWG Simulations NIRCam Edition
Jarron Leisenring
University of Arizona
July 19, 2021

## Slide 2: Comparison to WebbPSF Defaults
OTE OPDs and PSFs

## Slide 3: NIRCam Obs Configuration
NIRCam Coronagraphy
  MASK430R + F430M
  SUB320
  MEDIUM8, NG=7, NINT=50
  Exp time ~3600 sec
G2V source from BOSZ models
  Teff = 5777K
  logg = 4.43
  [Fe/H] = 0
  2MASS Ks = 3.27
Corresponds to ~100 million ph/sec through F430M bandpass

## Slide 4: OTE WFE Comparisons
Notes: WebbPSF comes with two FITS files, requirements.fits and predicted.fits.
Each FITS has 10 independent realizations.
These are based on measured flight mirror surfaces (for high spatial frequencies), plus statistical models for their alignment in flight following wavefront sensing and control (for mid and lower spatial frequencies)

## Slide 5: OTE WFE only – Direct Imaging PSF
Notes: Direct imaging PSF (F430M)
Includes stellar spectrum (total flux ~100M e-/sec)

## Slide 6: OTE WFE Comparisons + Lyot Mask
Notes: NIRCam Lyot stop for circular occulting masks

## Slide 7: OTE WFE only – Off-axis Coronagraphic PSFs
Notes: Off-axis PSFs also look very similar

## Slide 8: OTE WFE only – Occulted PSFs (MASK430R)
Notes: On-axis occulted Coronagraphic PSF (F430M + MASK430R)
New OPD shows much higher suppression compared to WebbPSF OPD
Primarily due to factor of ~1.5 lower RMS on the OPD map
Very distinct segment pattern

## Slide 9: Delta WFE components
The provided Thermal, Frill, and IEC maps are undersampled (100x100) and flipped compared to STATIC_***_INPUT.fits
Create new OPD at given time step
  Flip drift components up-down
  Rebin to 1024x1024
  Add to static OPD
Notes: Delta OPD
- requirements scenario
- after 3hrs
- added all three components together (frill and IEC dominate)

## Slide 10: PSF Differences (WFE Drift of 5.5 nm)
Notes: Improved blocking directly translates to lower speckle noise for the same WFE drift

## Slide 11: PSF Differences (TA offset of 10 mas)
Notes: Compare target acquisition offsets with same OPD maps.
Offset PSF is sub-pixel shifted
- Fourier imshift and cubic interpolation produce very similar results
- Linear interpolation does a poor job of sub-pixel shifting

## Slide 12: PSF Differences (TA + WFE drift)
Notes: Target acquisition offset of 10mas plus WFE drift of 5.5nm RMS
- Very similar speckle noise to just WFE drift of 5.5nm
- TA offsets ~10 mas therefore have negligible contributions

## Slide 13: Intermediate Conclusions (MASK430R)
Delivered OPD maps produce better coronagraphic suppression compared to WebbPSF’s *_predicted.fits and *_requirements.fits
  Should result in improved contrast at <2” by almost a factor of 2 (???)
WFE Drift vs Target Acquisition offsets
  TA offsets of 10 mas produce small residual speckle noise compared to WFE Drift of 5.5 nm RMS
  TA offsets may dominate for small WFE drifts, though
  Likely depends on mask and filter
Effects from jitter considered later…

## Slide 14: LOS Jitter
LOS Jitter values correspond to time steps every 37.7 sec
Jitter should be higher frequency (>1 Hz)
  Will blur PSFs over an integration time
  Enough samples over an exposure should also work
Adopt random jitter draws for each group (1.4 sec)
  Need 2 x 50 x 7 = 700
  Delivered LOS_JITTER.fits file does not provide enough independent values
  Generated appropriately sized random arrays using [2.5, 3.8, 5.8] mas per axis

## Slide 15: Observation Simulations
Using delivered OPD files (e.g., STATIC_***_INPUT.fits)

## Slide 16: NIRCam Obs Configuration
NIRCam Coronagraphy
  MASK430R + F430M
  SUB320
  MEDIUM8, NG=7, NINT=50
  Exp time ~3600 sec
G2V source from BOSZ models
  Teff = 5777K
  logg = 4.43
  [Fe/H] = 0
  2MASS Ks = 3.27
Corresponds to ~100 million ph/sec through F430M bandpass

## Slide 17: NIRCam Obs Configuration
NIRCam Coronagraphy
  MASK430R + F430M
  SUB320
  MEDIUM8, NG=7, NINT=50
  Exp time ~3600 sec
G2V source from BOSZ models
  Teff = 5777K
  logg = 4.43
  [Fe/H] = 0
  2MASS Ks = 3.27
Corresponds to ~100 million ph/sec through F430M bandpass
Notes: - Each INT receives an independent OPD map that is the sum of the three components (thermal, frill, IEC).
- Each group within an INT has an independent jitter draw in random direction with same statistical amplitude.
- For reference obs, there is a single target offset in (+X, +Y) for all INT
- Include WebbPSF’s static SI WFE
- The slew scenario here imparts a symmetry in thermal/frill drift that minimizes the average dWFE between sci and ref

## Slide 18: Results – Base Case (<dWFE> = 0.7 nm)
Notes: Left is a raw PSF
Middle is avg sci – avg ref
Right is avg sci – avg ref (aligned)

## Slide 19: Results – Nominal (<dWFE> = 1.3 nm)
Notes: Left is a raw PSF
Middle is avg sci – avg ref
Right is avg sci – avg ref (aligned)

## Slide 20: Results – Requirements (<dWFE> = 3.5 nm)
Notes: Left is a raw PSF
Middle is avg sci – avg ref
Right is avg sci – avg ref (aligned)

## Slide 21: Noise Components
Want to disentangle contributions from:
  WFE drift noise
  Jitter
  TA offsets
Calculate RMS of sci-ref differenced images
Generate contrast curves
Right: Case of jitter=0, TA=0.
Notes: Without jitter and TA, this simulation process shows very low residual speckle noise.
This is likely due on account of the small thermal timescales probed (sci=1hr, ref=1hr).
And the assumption of a symmetric slew/pitch angles.

## Slide 22
Average OPD drifts (nm RMS)
  Best, Nom, Req = (0.7, 1.3, 3.5)
Jitter & TA dominate residual speckle noise and contrast

## Slide 23
WFE Drift + Jitter
TA Offset

## Slide 24
Jitter
TA Offset
Notes: Constant WFE drift, changing jitter, changing TA

## Slide 25
Jitter
TA Offset
Notes: Constant WFE drift, changing jitter, changing TA

## Slide 26
Jitter
TA Offset
Notes: Constant WFE drift, changing jitter, changing TA

## Slide 27: Performance Metrics
WFE drift, jitter, and TA offset each contribute towards residual speckle noise.
Add contributions in quadrature.
Convert noise to contrast.
Notes: Distill images and contrast curves into performance metrics

## Slide 28: Performance Metrics
WFE drift, jitter, and TA offset each contribute towards residual speckle noise.
Add contributions in quadrature.
Convert noise to contrast.
Notes: Distill images and contrast curves into performance metrics

## Slide 29: Conclusions (MASK430R)
The simulated WFE drifts ( [0.7, 1.3, 3.5] nm RMS) have a minimal impact on the contrast relative to jitter and TA offsets.
  Low RMS of static OPD (compared to WebbPSF defaults)
  Small timescales probed (sci=1hr, ref=1hr)
  Assumed symmetric pitch angles for sci and ref slew (eg., +10 deg then -10 deg), which minimizes average drifts between the two observations.
Jitter
  For Nominal TA pointing, the range of jitter values (2.5-5.8 mas) produces a contrast difference of ~0.25 mag at 1”.
Target Acquisition Offsets
  For Nominal Jitter, contrast difference across TA: TA[12.5] – TA[6.3] = 0.4 mag